## Slide 1: OS 2021 Homework 4
Memory Manager
TA: 高靖智
E-mail: p76094088@gs.ncku.edu.tw
(Due day 2022/1/10 23:59:59) (Last Submission: 2022/1/15 23:59:59)
GitHub Classroom

## Slide 2: Background-Paging System with Multiple Processes
Overview of Memory Mapping with Multiple Processes
Physical Memory
Page Table
Process A
Process B
Process C
PFN
0
3
x
6
7
x
x
…
12
Frame 0
Frame 1
Frame 2
Frame 3
Frame 4
Frame 5
Frame 6
Frame 7
Frame 8
Frame 9
Frame 10
Frame 11
Frame 12
Frame 13
Frame 14
Frame 15
…
Frame M-1
Virtual Address Space
Process A
Process B
Process C
PFN
1
x
4
x
8
10
x
…
13
PFN
2
5
x
x
9
x
11
…
14
No
0
1
2
3
4
5
6
…
N-1
No
0
1
2
3
4
5
6
…
N-1
No
0
1
2
3
4
5
6
…
N-1

## Slide 3: Overview-Address Translation
Physical memory
M physical frames
PFN
5
29
139
23
...
CPU
1
VPN
0
M-1
...
...
29
...
...
Page Table
N virtual pages
VPN: Virtual Page Number PFN: Physical Frame Number
v_addr
VPN | PFN
2 | 139
0 | 5
1 | 29
TLB Miss
TLB
TLB Hit
A paging based memory manager with TLB support
Done by hardware
No
0
1
2
N-1
...

## Slide 4: Overview-Page Fault Handler (1/2)
Physical Memory
Page Table
Process A
PFN
0
3
x
6
7
x
x
…
12
Frame 0
Frame 1
Frame 2
Frame 3
Frame 4
Frame 5
Frame 6
Frame 7
Frame 8
Frame 9
Frame 10
Frame 11
Frame 12
Frame 13
Frame 14
Frame 15
…
Frame M
Once a page fault occurs
  If there are free frames in physical memory
    Allocates physical frame and fills in PFN for the page table
    A system-wide free frame list is maintained by the OS
Free-Frame List
Frame 8
Frame 10
Frame 13
Frame 15
Reference(page 2)
Page fault
Page Fault Handler
8
Frame 8
Done by OS kernel
No
0
1
2
3
4
5
6
…
N-1

## Slide 5: Overview-Page Fault Handler (2/2)
Physical Memory
Page Table
Process A
PFN
0
3
x
6
12
x
x
…
7
Frame 0
Frame 1
Frame 2
Frame 3
Frame 4
Frame 5
Frame 6
Frame 7
Frame 8
Frame 9
Frame 10
Frame 11
Frame 12
Frame 13
Frame 14
Frame 15
…
Frame M
Once a page fault occurs
  If there is no free frame in physical memory
    Evicts a page (i.e., the victim) to the disk
    The victim selection is based on certain replacement policy.
Reference(page 2)
Page fault
Page Fault Handler
Page 8
Page 10
Page 4
Page 14
Replacement List
…
victim page
evict to disk
Frame 8
8
Frame 8
Disk
No
0
1
2
3
4
5
6
…
N-1
Done by OS kernel
Process C
Process B
Process A

## Slide 6: Overview-Allocation Policy (1/2)
Physical Memory
Page Table
Process A
PFN
0
3
x
6
7
x
x
…
12
Frame 0
Frame 1
Frame 2
Frame 3
Frame 4
Frame 5
Frame 6
Frame 7
Frame 8
Frame 9
Frame 10
Frame 11
Frame 12
Frame 13
Frame 14
Frame 15
…
Frame M
Global
  When a page fault occurs in process ‘X’ , any page frame (either from ‘X’ or the other processes) can be the victim page
Reference(page 2)
Page fault
Page Fault Handler
Page 5
Page 8
Page 11
Page 15
Global Replacement List
…
victim page
evict to disk
No
0
1
2
3
4
5
6
…
N-1
Disk
Process C
Process B
Process A

## Slide 7: Overview-Allocation Policy (2/2)
Physical Memory
Page Table
Process A
PFN
0
3
x
6
7
x
x
…
12
Frame 0
Frame 1
Frame 2
Frame 3
Frame 4
Frame 5
Frame 6
Frame 7
Frame 8
Frame 9
Frame 10
Frame 11
Frame 12
Frame 13
Frame 14
Frame 15
…
Frame M
Local
  When a page fault occurs in process ‘X’, the victim can be selected only from process ‘X’
Reference(page 2)
Page fault
Page Fault Handler
Page 1
Page 3
Page 4
Page N-1
Process A’s Replacement List
…
victim page
evict to disk
No
0
1
2
3
4
5
6
…
N-1
Disk

## Slide 8
Overview-Memory Manager (1/5)
1
VPN
Process A Page Table
VPN | PFN
4 | 7
3 | 20
1 | 0
TLB
TLB Hit
trace.txt
Physical Memory
Frame 0
Frame 1
Frame 2
Frame 3
Frame 4
Frame 5
Frame 6
Frame 7
Frame 8
Frame 9
Frame 10
Frame 11
Frame 12
Frame 13
Frame 14
Frame 15
…
Frame M
Reference(A, 1)
Reference(A, 0)
Reference(A, 2)
Reference(B, 1)
Page Fault Handler
Per Process/Global Replacement List
…
victim page
No
1
2
3
4
5
6
…
N-1
Disk
Frame x
Frame x
Frame x
…
Free-Frame List
0
trace_output.txt
  Process A, TLB Hit, 1=>0
Access information for each reference
Page 3
Page 6
Page 4
Process C
Process B
Process A
Overview of Memory Manager
  TLB Replacement Policy: LRU
  Page Replacement Policy: FIFO
  Frame Allocation Policy: GLOBAL
  Number of Processes: 3
  Number of Virtual Page: 2048
  Number of Physical Frame: 1024
sys_config.txt
PFN
3
0
x
6
7
x
x
…
12

## Slide 9
Overview-Memory Manager (2/5)
0
VPN
Process A Page Table
VPN | PFN
4 | 7
3 | 20
1 | 0
TLB
trace.txt
Physical Memory
Frame 0
Frame 1
Frame 2
Frame 3
Frame 4
Frame 5
Frame 6
Frame 7
Frame 8
Frame 9
Frame 10
Frame 11
Frame 12
Frame 13
Frame 14
Frame 15
…
Frame M
Reference(A, 1)
Reference(A, 0)
Reference(A, 2)
Reference(B, 1)
Page Fault Handler
Per Process/Global Replacement List
…
victim page
No
1
2
3
4
5
6
…
N-1
Disk
Frame x
Frame x
Frame x
…
Free-Frame List
0
trace_output.txt
  Process A, TLB Hit, 1=>0
  Process A, TLB Miss, Page Hit, 0=>3
  Process A, TLB Hit, 0=>3
Access information for each reference
Page 3
Page 6
Page 4
Process C
Process B
Process A
Overview of Memory Manager
  TLB Replacement Policy: LRU
  Page Replacement Policy: FIFO
  Frame Allocation Policy: GLOBAL
  Number of Processes: 3
  Number of Virtual Page: 2048
  Number of Physical Frame: 1024
sys_config.txt
TLB Miss
Page Hit
PFN
3
0
x
6
7
x
x
…
12
0
3
TLB Hit
update TLB entry

## Slide 10
Overview-Memory Manager (3/5)
2
VPN
Process A Page Table
VPN | PFN
4 | 7
3 | 20
1 | 0
TLB
trace.txt
Physical Memory
Frame 0
Frame 1
Frame 2
Frame 3
Frame 4
Frame 5
Frame 6
Frame 7
Frame 8
Frame 9
Frame 10
Frame 11
Frame 12
Frame 13
Frame 14
Frame 15
…
Frame M
Reference(A, 1)
Reference(A, 0)
Reference(A, 2)
Reference(B, 1)
Page Fault Handler
Per Process/Global Replacement List
…
victim page
No
1
2
3
4
5
6
…
N-1
0
Disk
Frame x
Frame x
Frame x
…
Free-Frame List
0
trace_output.txt
  Process A, TLB Hit, 1=>0
  Process A, TLB Miss, Page Hit, 0=>3
  Process A, TLB Hit, 0=>3
  Process A, TLB Miss, Page Fault, 6, Evict 3 of Process A to 0, 2 << -1
  Process A, TLB Hit, 2=>6
Access information for each reference
Page 3
Page 6
Page 4
Process C
Process B
Process A
Overview of Memory Manager
  TLB Replacement Policy: LRU
  Page Replacement Policy: FIFO
  Frame Allocation Policy: GLOBAL
  Number of Processes: 3
  Number of Virtual Page: 2048
  Number of Physical Frame: 1024
sys_config.txt
TLB Miss
Page fault
evict to disk
PFN
3
0
x
6
7
x
x
…
12
2
6
TLB Hit
update TLB entry

## Slide 11
PFN
1
4
x
8
10
x
x
…
15
Overview-Memory Manager (4/5)
VPN
Process B Page Table
VPN | PFN
4 | 7
3 | 20
1 | 0
TLB
trace.txt
Physical Memory
Frame 0
Frame 1
Frame 2
Frame 3
Frame 4
Frame 5
Frame 6
Frame 7
Frame 8
Frame 9
Frame 10
Frame 11
Frame 12
Frame 13
Frame 14
Frame 15
…
Frame M
Reference(A, 1)
Reference(A, 0)
Reference(A, 2)
Reference(B, 1)
Page Fault Handler
Per Process/Global Replacement List
…
victim page
No
1
2
3
4
5
6
…
N-1
Disk
Frame x
Frame x
Frame x
…
Free-Frame List
0
trace_output.txt
  Process A, TLB Hit, 1=>0
  Process A, TLB Miss, Page Hit, 0=>3
  Process A, TLB Hit, 0=>3
  Process A, TLB Miss, Page Fault, 6, Evict 3 of Process A to 0, 2 << -1
  Process A, TLB Hit, 2=>6
Access information for each reference
Page 3
Page 6
Page 4
Process C
Process B
Process A
Overview of Memory Manager
  TLB Replacement Policy: LRU
  Page Replacement Policy: FIFO
  Frame Allocation Policy: GLOBAL
  Number of Processes: 3
  Number of Virtual Page: 2048
  Number of Physical Frame: 1024
sys_config.txt
Flush TLB Entry
Change PTBR
Switch Process

## Slide 12
PFN
1
4
x
8
10
x
x
…
15
Overview-Memory Manager (5/5)
1
VPN
Process B Page Table
VPN | PFN
X | X
X | X
X | X
TLB
trace.txt
Physical Memory
Frame 0
Frame 1
Frame 2
Frame 3
Frame 4
Frame 5
Frame 6
Frame 7
Frame 8
Frame 9
Frame 10
Frame 11
Frame 12
Frame 13
Frame 14
Frame 15
…
Frame M
Reference(A, 1)
Reference(A, 0)
Reference(A, 2)
Reference(B, 1)
Page Fault Handler
Per Process/Global Replacement List
…
victim page
No
1
2
3
4
5
6
…
N-1
Disk
Frame x
Frame x
Frame x
…
Free-Frame List
0
trace_output.txt
  Process A, TLB Hit, 1=>0
  Process A, TLB Miss, Page Hit, 0=>3
  Process A, TLB Hit, 0=>3
  Process A, TLB Miss, Page Fault, 6, Evict 3 of Process A to 0, 2 << -1
  Process A, TLB Hit, 2=>6
  Process B, TLB Miss, Page Hit, 1=>4
  Process B, TLB Hit, 1=>4
Access information for each reference
Page 3
Page 6
Page 4
Process C
Process B
Process A
Overview of Memory Manager
  TLB Replacement Policy: LRU
  Page Replacement Policy: FIFO
  Frame Allocation Policy: GLOBAL
  Number of Processes: 3
  Number of Virtual Page: 2048
  Number of Physical Frame: 1024
sys_config.txt
TLB Miss
Page Hit
  Process A, Effective Access Time = 150 Process B, Effective Access Time = 75 Process A, Page Fault Rate: 0.800
  Process B, Page Fault Rate: 0.770
analysis.txt
Based on the access information, generate the analysis for each process
1
4
TLB Hit
update TLB entry

## Slide 13: Requirements (1/2)
Implement a paging based memory manager with TLB support
  Allocate/manage physical frames for multiple processes
  Use a TLB to speed up address translation by software simulation
  Use an one-level page table for mapping virtual pages to physical frames
When the page table has been updated
  Ensure that TLB/page table are consistent
When the process has been switched
  Flush TLB and change PTBR
TLB Replacement Policy
  Random
  LRU
Page Replacement Policy
  FIFO
  Clock
Frame Allocation Policy
  Global
  Local

## Slide 14: Requirements (2/2)
Show the TLB miss/hit and related information for each reference in trace file on the output file.
  If a TLB miss occurs, show the page hit/page fault and related information for each reference in trace file on the output file.
Show the following information for each process under different policies
  Effective Access Time
  Page Fault Rate
Write a document to show the pros and cons of each policy
  Please describe your own opinions

## Slide 15: Requirement-Page Table
Reference Bit
  1: the page table entry is referenced
  0: the page table entry is not referenced
Present Bit
  1: the page is in physical memory
  0: the page is not in physical memory, it is on disk
When a page is page-out to disk block K, the PFN field will be set as K
VPN | PFN/DBI | Reference | Present
0 | 4 | 1 | 0
1 | 0 | 1 | 0
2 | 0 | 0 | 0
… |  |  | 
Z | 2 | 1 | 1
VPN : virtual page number
PFI : physical frame number
DBI : disk block number

## Slide 16: Assumptions
The number of TLB entries is fixed to 32
  There is no ASID support in this homework assignment
There will be P processes, N virtual pages and M physical frames
  P, N and M will be given in the trace file
  N is greater than M
  N and M are both power of 2
Page fault handler only evicts a page to the disk when there is no free frame in physical memory
An evicted page should be written back to the disk whether it is dirty or not
  This is not the case in real world, but it simplifies the complexity of this homework
The disk always has enough space for evicted pages
  To page-out a page, select an free disk block with the smallest disk block number

## Slide 17: Input File Format (1/2)
Two input files: system configuration file and trace information file
System configuration file
  File name: “sys_config.txt”
  Includes 6 lines
    Which TLB Replacement Policy?
    Which Page Replacement Policy?
    Which Frame Allocation Policy?
    Number of Process?
      20 ≧ P ≧ 1
    Number of Virtual Page N
      2048 ≧ N ≧ 2
      Power of 2
    Number of Physical Frame M
      1024 ≧ M ≧ 1
      N ≧ M
      Power of 2
  1 TLB Replacement Policy: LRU | Random
  2 Page Replacement Policy: FIFO | CLOCK
  3 Frame Allocation Policy: LOCAL | GLOBAL
  4 Number of Processes: P (>=1)
  5 Number of Virtual Page: N (power of 2)
  6 Number of Physical Frame: M (power of 2)
sys_config.txt

## Slide 18: Input File Format (2/2)
Trace information file
  File name: “trace.txt”
  Includes page reference information of the processes
  Reference (X, Y): reference virtual page Y of Process X
  X ranges from ‘A’ ~ ‘T’
  1 Reference(A, 0)
  2 Reference(A, 1)
  3 Reference(A, 2)
  4 Reference(B, 0)
  5 Reference(B, 1)
  6 Reference(B, 2)
  7 Reference(C, 0)
  8 Reference(C, 1)
  9 Reference(C, 2)
  …
  2 Reference(B, 4)
  …
  Z Reference(C, 8)
trace.txt

## Slide 19: Output File Format (1/2)
Show the following information for each reference
  Format for a TLB hit: Process [X], TLB Hit, [VPN]=>[PFN]
  Format for a TLB miss:
    Page hit: Process [X], TLB Miss, Page Hit, [VPN]=>[PFN]
    Page fault: Process [X], TLB Miss, Page Fault, [PFN], Evict [VPN] of Process [X] to [Destination], [VPN]<<[Source]
    PFN: frame index that is about to be replaced
    Source: the block number of the page which is page-in from disk
    Destination: the block number where the evicted page page-out
  If there is no source/destination (e.g., first reference, no page is page-out) or no evicted VPN, set the value as -1
Store as “trace_output.txt”
  Process A, TLB Miss, Page Fault, 0, Evict -1 of Process A to -1, 6 << -1
  Process A, TLB Hit, 6=>0
  …
  Process A, TLB Miss, Page Hit, 1=>6
  …
  Process B, TLB Miss, Page Hit, 2=>10
trace_output.txt

## Slide 20: Output File Format (2/2)
Show the Effective access time for each process
  EAT = α(m+t) + (1- α)(2m+t)
  Assume
    m = 100ns
    t = 20ns
Show the page fault rate for each process
Store as `analysis.txt`
TLB Lookup time = t time units
Memory cycle time = m time units
Hit ratio = α
  Process A, Effective Access Time = 191.428 Process A, Page Fault Rate: 0.800
  Process B, Effective Access Time = 160.725 Process B, Page Fault Rate: 0.770
analysis.txt
three decimal place accuracy